## Slide 1: Wireless Network and Layering
Chapter 3

## Slide 2: The Internet
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 3: The Internet
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Internet standards
  IEEE
  IETF: Internet Engineering Task Force

## Slide 4: Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  Hosts
  Routers
  Links of various media
  Applications
  Protocols
  Hardware, software
Question: Is there any hope of organizing structure of network?
and/or our discussion of networks?

## Slide 5: Why layering?
Layering is used to organize the various functions of data communications by breaking the distinct functions into a different Layers
Modularization eases maintenance, updating of system
  Change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 6: TCP/IP Model
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 7: Services, Layering and Encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M

## Slide 8: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer packet
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 9: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using network-layer services
M
Ht
Hn
Hl
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 10: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
Ht
M
M
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
message
segment
packet
frame
M
Ht
Hn
Hl

## Slide 11: Encapsulation: an end-end view
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
packet
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical

## Slide 12: ISO/OSI reference model
The Open Systems Interconnection (OSI) model is a conceptual model like TCP/IP model,used to organize the various functions of data communications by breaking the distinct functions into a seven-layer
Two layers not found TCP/IP Model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model

## Slide 13: Wireless Network and Layering
All Wireless LANs operate on the Physical and Data Link layers, layers 1 and 2
All Wireless systems use these layers to format data and control the data to conform with wireless standards

## Slide 15: Data Link Layer
The data link layer is an interface between the network and physical layer. The Data Link layer is responsible for organizing the bit-level data for communication between devices on a network and detecting and correcting Physical layer errors. also it is responsible for the multiplexing of data streams and data frame detection
It is further subdivided into two modules:
  Medium Access Control (MAC) plays a critical role in conserving network life by efficiently allocating medium access to the contending nodes.
  Logical Link Control (LLC) is on top of the MAC layer and is responsible for cyclic redundancy check (CRC), sequencing information, and addition of appropriate source and destination information.

## Slide 16: Datalink layer - LLC
LLC layer lets the upper layers communicate with any form of transmission media in the same way.
Flow Control, it control the rate of data transmission between two sources and destination hosts
Error detection and correction
LLC layer protocols include specifications for the frames of many types of physical networks, including Ethernet, WIFI, FDDI (Fiber Distributed Data Interface).

## Slide 17: Datalink layer -MAC
It maintains, and manages the communications between the access points (AP) and the 802.11 clients.
Coordinate the access to the shared radio channel for all the devices

## Slide 18: The Physical Layer
    Physical Layer Convergence Protocol(PLCP): frame exchange between the MAC and PHY, used to indicate data rates and packet length.
    Physical Medium Dependent(PMD): uses signal carrier and modulation to transmit data frames over the media.
      This service interfaces directly to the RF.
      It modulates/demodulates (MODEM) the frame transmissions.
      The examples of modulation are : Direct Sequence Spread Spectrum (DSSS) PHY, The Frequency Hopping Spread Spectrum (FHSS) PHY, AM and FM modulation.