## Slide 2: Objectives
Discuss basic networking technologies
Describe the infrastructure of the Internet, including network service providers, the TCP/IP stack, IP addresses, and the Domain Name System (DNS)
Discuss GPS and identify wireless location-based services

## Slide 3: Objectives
Explain the convergence of the Internet with telephony and conferencing
Discuss internal and external network security threats, transactional risks, and virtual private networks

## Slide 4: Networking Basics
A network connects two or more computers, printers, or other devices together with cables or wireless media allowing users to share
  Data
  Peripheral devices
  Software and apps
  Other network resources (such as an Internet connection)

## Slide 5: Networking Basics
Local, Metropolitan, and Wide Area Networks
  Modern networks can be categorized by the physical area they cover
    Local area network (LAN) - home, office, building, or several buildings
    Metropolitan area network (MAN) – region
    Wide area network (WAN) - across the country or around the world
Local Area Networks
  Local area networks are configured in one of two basic structures
    Peer-to-peer
    Client/server

## Slide 6: Networking Basics
Local Area Networks (continued)
  Peer-to-peer LAN
    10 or fewer personal computers connected
    One or more of the computers may also have a printer, scanner, or external storage device
    Each node must have built-in networking capabilities or a network interface card (NIC)
    Each node may be connected to a single cable or may be connected at a common connection point using a hub
    Users can access files stored on any computer and any peripheral device connected to a computer on the network
    Simple to configure and inexpensive to use

## Slide 7: Networking Basics

## Slide 8: Networking Basics
Local Area Networks (continued)
  Client/server network consists of multiple personal computers and devices or workstations (clients), one or more servers, and other devices such as printers
  Uses a network operating system to manage data, printer access, communications, Internet connections, security, and network administration
  Examples include Microsoft Windows Server, OS X Server, Novell NetWare, Cisco IOS, UNIX, and Linux

## Slide 9: Networking Basics
Local Area Networks (continued)
  Advantages over a peer-to-peer network
      Supports shared data storage
      Provides network maintenance tools
      Promotes more efficient data backups
  Disadvantages compared to a peer-to-peer network
      More expensive
      More difficult to configure
      Requires more technical expertise to manage

## Slide 10: Networking Basics

## Slide 11: Networking Basics
Metropolitan Area Networks (MANs)
  Connects clients and servers in a region that is larger than a single office or building
    Multiple buildings across a city or multiple educational, research, or government facilities across a state
  Generally are owned by a consortium of users of a single network provider that sells high-speed network services to multiple users

## Slide 12: Networking Basics
Wide Area Networks (WANs)
  Cover a very wide geographical area
    Can be a single network or multiple connected LANs located across the country or around the world
    Most WANs are private, corporately owned networks
    The Internet is the world’s largest public WAN

## Slide 13: Networking Basics
Network Topologies, Access Methods, and Transmission Media
  Physical topology is the arrangement of a network’s computers, printers
  Access method is how data is transmitted from node to node across the network
  Transmission media – are the physical or wireless communication media used to carry transmissions
  These three characteristics define the throughput, which is the amount of data that can travel node to node in a specified amount of time

## Slide 14: Networking Basics
Network Topologies, Access Methods, and Transmission Media (continued)
  Three basic LAN physical topologies
    Bus
    Ring
    Star
  Today, many LANs use a hybrid physical topology that combines some elements of these three topologies

## Slide 15: Networking Basics
Network Topologies, Access Methods, and Transmission Media (continued)
  Access Methods
    Sometimes called logical topology
    Ethernet – a node attempting to transmit data first must determine whether or not another node is sending a transmission
    Token ring – passes tokens, small packets of data, clockwise in a circle from node to node
  Transmission Media
    Cellular transmissions travel wirelessly over land cells using transceivers, or cell sites; cellular networks can transfer voice and data over a large, almost limitless area

## Slide 16: Networking Basics

## Slide 17: Networking Basics
Network Topologies, Access Methods, and Transmission Media (continued)
  Transmission Media (continued)
    Infrared (IR) transmissions use infrared light-wave signals as short range transmission medium; require line-of-sight transmissions
    Near field communication (NFC) transmissions use radio waves to connect devices that are touching or nearby (generally within 10 centimeters)

## Slide 18: Networking Basics
Network Topologies, Access Methods, and Transmission Media (continued)
  Transmission Media (continued)
    Radio frequency (RF) transmissions use broadcast radio waves to transmit data over short distances; some wireless devices use transceiver, a single component and receives transmissions
    Bluetooth is a short-range RF technology
      Designed for wireless personal area networks (WPANs), which have a range of approximately 33 feet (10 meters)
      To enable two Bluetooth devices to work together, pair them

## Slide 19: Networking Basics
Network Topologies, Access Methods, and Transmission Media (continued)
  Transmission Media (continued)
    A Wi-Fi network, or wireless LAN (WLAN) uses a wireless medium — such as radio frequency transmissions — to connect computers and mobile devices, printers, and other devices
    Physical transmission media
      Coaxial cable (pronounced KO-ax); although was the choice for many early networks, not used in most modern networks because it does not transmit data as fast as other media
      Twisted-pair cable commonly used as a LAN transmission medium
      Fiber-optic cable commonly used as a MAN or WAN transmission medium

## Slide 20: Networking Basics

## Slide 21: Networking Basics
Connectivity Hardware and Software
  Hardware connectivity devices connect nodes on the same network, connect nodes across multiple networks, and forward packets between nodes
  Segments are multiple groups of computers or devices that share a common function
  Hubs
    Hub – inexpensive hardware device used to connect multiple nodes on the same network
      Passive hub – cannot determine how to direct a packet; simply sends same signal to all its connected nodes or segments
      Intelligent hub – can perform tasks, such as filtering data or permitting a network administrator to monitor hub traffic

## Slide 22: Networking Basics
Connectivity Hardware and Software (continued)
  Bridges
    Bridge – intelligent connectivity device with one input port and one output port that connects two segments on the same LAN or two separate LANs
    Each node on the network has a MAC (Media Access Control Address)
    Bridge creates a database of all the MAC addresses for nodes on its segment or LAN
  Data Switches
    Data switch – intelligent device that also interprets MAC addresses and filters and forwards data packets to network segments
    Can be a less-expensive choice than a bridge for networks with a large number of nodes

## Slide 23: Networking Basics
Connectivity Hardware and Software (continued)
  Routers
    Router is an intelligent device with multiple ports; a specialized computers that connect LAN segments, two LANs, or multiple LANs on a WAN
      Determines the best route for packets
      Fall into three categories: wireless, mobile, or broadband
      Use static routing or dynamic routing
      Internet routers are complex, fast, expensive devices that send packets from one router to another in a series of hops until they reach their destination network
      Use the tracert utility to trace router hops

## Slide 24: Using the Tracert Utility to Trace Hops
Press and hold or right-click the Start button on the Windows taskbar.
Tap or click the Run menu command to open the Run dialog box.
Enter cmd in the Open text box in the Run window.
Tap or click the Open button, or press the ENTER key to open the Command Prompt window.
Enter tracert www.cengage.com at the command-line prompt to trace the number of hops between your computer and the destination computer.
Press the ENTER key to view the path from your computer to the Cengage destination server as packets are sent from router to router over the Internet.

## Slide 25: Using the Tracert Utility to Trace Hops

## Slide 26: Networking Basics
Connectivity Hardware and Software (continued)
  Gateways
    A gateway is a hardware or software that runs on a mainframe computer, server, individual workstation or router; connects two or more networks or network segments that use different packet formatting, different communication protocols, and different access methods

## Slide 27: Internet Infrastructure
Network Service Providers
  Network service providers (NSPs) provide the public and private network infrastructure for the Internet that enables wireless, cellular, and other capabilities
    AT&T, Sprint, Verizon, T-Mobile, and others
  An Internet exchange point (IXP) is a physical infrastructure that enables ISPs to communicate among their networks, which limits the upstream traffic an ISP must handle
    Metropolitan Area Exchange (MAE) – a specific type of high-speed Ethernet connection within a metropolitan area
  Peering is the exchange of Internet traffic and router information between NSPs and ISPs at an exchange point

## Slide 28: Internet Infrastructure
TCP/IP Stack
  TCP/IP stack –set of standard Internet protocols on which communications across the Internet and many private networks rely
    TCP, IP, and UDP are core subprotocols required for all TCP/IP transmissions
  IP network is another name for a network running TCP/IP

## Slide 29: Internet Infrastructure
IP Addresses
  In addition to a MAC address, each node on an IP network has a logical address, called an IP address
  IP address is the unique address of each node on a network
    The current IP standard, IPv6, lengthens IP addresses from 32 bits to 128 bits
    Contains eight 8-bit numbers, each of which is called an octet

## Slide 30: Internet Infrastructure

## Slide 31: Internet Infrastructure
IP Addresses (continued)
  Classful routing system used originally
  Classless routing system, called Classless Inter-Domain Routing (CIDR) allows network administrators to expand the number of network nodes assigned to an IP address
    Used extensively on the Internet
    Used in large private networks

## Slide 32: Viewing a Networked Computer’s IP Address
Open the Command Prompt window.
Enter ipconfig /all at the command-line prompt to instruct the operating system to display all IP information about your networked computer.
Press the ENTER key to display your computer’s host name, IP address, and other IP information.

## Slide 33: Internet Infrastructure
Domain Name System (DNS)
  The DNS is a hierarchy of servers used to translate domain names into IP addresses in a process called resolving the domain name
  Twelve different organizations, such as VeriSign, NASA, the University of Maryland, and the University of Southern California, operate the root name servers

## Slide 34: Internet Infrastructure
Domain Name System (DNS) (continued)
  Authoritative servers contain IP information for the TLD and ccTLD domains and their registrants
  Caching servers operated by ISPs and company IT departments contain stored domain name and IP address information
  DNS namespace consists of all information in the DNS databases
  Process of resolving a domain name begins with local caching server

## Slide 35: Internet Infrastructure

## Slide 36: Internet Infrastructure
Domain Name System (DNS) (continued)
  Shared Registration System (SRS) is registration system that allows private companies, called accredited registrars, to handle registration of domain names

## Slide 37: Internet Infrastructure
Domain Name System (DNS) (continued)
  Process of registering domain name varies by registrar
  If chosen name is taken, reconsider website name

## Slide 38: Location-Based Services and GPS
Location-based service (LBS) is a wireless service offered to customers based on their physical location
  Example: E9-1-1
Global Positioning System (GPS) satellite network and receivers mounted in automobiles or placed in mobile phones, watches, tablets, or other handheld devices
  32 satellites
  11,000 miles above earth

## Slide 39: Location-Based Services and GPS
Geosocial networking is a term used to describe the combination of LBS with social networking providers

## Slide 40: Internet Telephony and Web Conferencing
Internet Telephony
  IP telephony or Voice over IP (VoIP)
  Uses TCP/IP and packet switching to send voice transmissions over private or public IP network
    VoIP providers, such as Vonage, offer telephone services to homes and businesses over broadband Internet connections.
    Computer to computer calling using special software, such as Skype

## Slide 41: Internet Telephony and Web Conferencing
Virtual Meetings, Conversations, and Web Conferencing
A virtual meeting allows collaboration between participants, such as a group of employees, by allowing invitees to log on to their network and sign in to a meeting in which they communicate with each other as well as view, share, and work collaboratively on files
Video conferencing, an expanded virtual meeting that sometimes includes hundreds or thousands of participants, involves real-time transmission of video and audio between two locations

## Slide 42: Internet Telephony and Web Conferencing
Virtual Meetings, Conversations, and Web Conferencing
A virtual conversation is a video chat using services such as Google Hangouts or FaceTime
Web conferencing is a virtual meeting conducted using a browser and the web

## Slide 43: Network Security Issues and Technologies
Internal Network Security Threats
  Security Policies and Procedures
  Authorized Network Access
    User ID and passwords (something you remember)

## Slide 44: Network Security Issues and Technologies
Internal Network Security Threats (continued)
  Biometrics – using devices to measure biological data to identify a user (something you are)
  Smart card – plastic card the size of a credit card that contains memory chips that can store special access codes or biometric information (something you have)
  Wireless Network Security
    LAN jacking or war driving
    Spoofing
    Rogue WLAN
  Data Storage, Backup, and Restore
    Cloud storage

## Slide 45: Network Security Issues and Technologies
Internal Network Security Threats (continued)
  Disaster Recovery Planning
    Techniques to protect against accidental or deliberate physical damage to network equipment and data
    Disaster recovery plan covers how an organization deals with a natural or man-made disaster to ensure the organization’s viability
External Network Security Threats
  Unauthorized Network Access
    Distributed denial of service (DDoS) attacks
    Hackers may break into network to steal account information, such as credit card numbers, user passwords, and other personal information to steal a person’s identity, make unauthorized credit card purchases, or open accounts in a user’s name for illegal purposes

## Slide 46: Network Security Issues and Technologies
External Network Security Threats (continued)
  Computer Viruses
  Worm
  Trojan horse
  Protect again viruses with virus protection apps
    Symantec
    McAfee
    Swipe codes

## Slide 47: Reviewing Current Virus, Worm, and Trojan Horse Threats
Enter symantec.com in browser’s Address bar and then press the ENTER key or tap or click the appropriate button to open the Symantec webpage.
Tap or click the Security Response link to open the webpage.
Tap or click the Threats tab.

## Slide 48: Network Security Issues and Technologies
External Network Security Threats (continued)
  Web Page Hacking
    Hijacking occurs when hackers redirect a URL to an alternate website
    Web Application Security Consortium and its sponsored Web Hacking Incidents Database is a good learning resource

## Slide 49: Network Security Issues and Technologies
External Network Security Threats (continued)
  Firewalls and Proxy Servers
    Network firewall is a combination of hardware and software that filters traffic between private networks or between a private network and a public network, such as the Internet
    Proxy server is a computer or application that hides an internal IP address from the outside world by substituting its own IP address for a source computer’s IP address before sending outgoing email or webpage requests

## Slide 50: Network Security Issues and Technologies

## Slide 51: Network Security Issues and Technologies
External Network Security Threats (continued)
  Internet Filtering Software
    WebSpy
    Websense
  Security Audits
    Network security audit – reviews overall security policies, employee security policy and procedure training, data backup and restore policies and procedures, and the physical security of network equipment and data
    Penetration testing – security audit personnel try to hack into network

## Slide 52: Network Security Issues and Technologies
Transactional Risks
  Authentication, integrity, nonrepudiation, confidentiality
  Encryption – translating readable data into unreadable data to prevent unauthorized access or use
  Certificate authority (CA) creates encryption keys (public and private) for a fee
    Public key encrypts data and is posted by CA to publicly accessible directory
    Private key is known only to organization and is used to decrypt incoming data

## Slide 53: Network Security Issues and Technologies
Transactional Risks (continued)
  Digital certificate electronically authenticates organization’s or individual’s identity

## Slide 54: Network Security Issues and Technologies
Transactional Risks (continued)
  Public key infrastructure is combination of organizations or individuals sending and receiving encrypted data, their public and private keys, and the CAs that issue the keys and digital certificates.

## Slide 55: Virtual Private Networks
A virtual private network uses a large public IP network, such as the Internet, to transmit its data
  Tunneling is a process that encapsulates one protocol inside another protocol
  At destination network, the IP protocol information is removed and the tunneling protocol transmits the data to its final destination computer
  VPNs also use public and private key encryption, digital certificates and special security protocols

## Slide 56: Summary
Discuss basic networking technologies
Describe the infrastructure of the Internet, including network service providers, the TCP/IP stack, IP addresses, and the Domain Name System (DNS)
Discuss GPS and identify wireless location-based services

## Slide 57: Summary
Explain the convergence of the Internet with telephony and conferencing
Discuss internal and external network security threats, transactional risks, and virtual private networks